## Slide 1: API Development for Forecasting Solar Power Generation Using Weather Data
Presented by :
Muhammad Miftah Faridh
Department of Electronics Engineering
Kookmin University
THE 33rd JOINT CONFERENCE ON COMMUNICATIONS AND INFORMATION

## Slide 2
Outline
General Overview
Motivation & Contribution
Methodology
System Overview
Result & Discussion
Conclusion

## Slide 3
General Overview
  Because of the current reliance on fossil fuels, the human population will confront a catastrophic energy crisis [1].
  Solar energy can considerably contribute to the world's electricity needs [2].
  PV solar panels are mostly dependent on the regular pattern of solar irradiation. The radiation magnitude is zero at night, increases at dawn, and decreases at night. In addition, the weather conditions at certain times, which will block sun energy, will have an effect [3].

## Slide 4
The time series model is one of this study's most commonly employed algorithms, although it has several distinct limitations.
Due to this, numerous algorithms are employed in solar forecasting, including statistical time series models and artificial neural networks (ANNs) which have recently gained widespread acceptance for renewable energy forecasts.
LSTM, Bi-LSTM, Stacked Bi-LSTM, RNN, and GRU models were used to produce forecasts based on solar power generation and weather data from different regions in Korea.
Motivation & Contribution
Weather & Energy Data
Comparison Model
Forecast Model

## Slide 5
Methodology
We collect PV sites in many regions of Korea, including Busan, Seoul, Gyeonggi, Gangwon, Daejeon, Gyeongnam, Jeonbuk, Sejong, Chungbuk, and Chungnam, for the production of solar power electrical statistics.
The data is then sent to the database via MQTT.
We require weather data to train the model; this data is available via the open API of the Korea Meteorological Administration (KMA). The data we collect is hourly data for the entire year of 2021.
Figure 1. Develop Solar Power Generation Forecasting Using Weather Data

## Slide 6
Data Preprocessing
Interpolate Missing value using interpolation with nearest method.
System Overview

## Slide 7
Data Preprocessing
Deletion the outlier data and replace with nearest data
System Overview
Then, the data are normalized using the MinMax method, the -1 to 1 rescaling approach

## Slide 8
Data Preprocessing
System Overview
Correlation checking uses a correlation matrix and takes features that have the highest correlation, and we get temperature, relative humidity, solar radiation, sunshine in seconds per hour, and precipitation per hour as the highest correlation

## Slide 9
System Overview
We used 1 Month data to predict 1 week future data
Windows
1 Month Data
1 Week
Test Data
Data Preprocessing

## Slide 10
Deep learning model based on Power Generation forecasting
System Overview
We set the batch size to 32, the hyperparameter Adam as the optimizer with a learning rate of 0.001, the iteration to 200, and the callback function to terminate if the data has already reached convergence or is close to overfitting.
Weather Data
Power Generation Data
Pre Processing
Forecast Trained Model
LSTM, Bi-LSTM, Stacked Bi-LSTM, RNN, and GRU.

## Slide 11
Deep learning model based on Power Generation forecasting
System Overview
We present several findings regarding the predicted timeliness of time series data. Loss, validation loss, and mean square error (MSE) are the essential measures for evaluating a model's quality. The RMSE, the mean absolute error (MAE), and the regression score (R-squared or R2 score) were used to evaluate the accuracy of the predictions. We use above equation to determine the error metrics.

## Slide 12
Result and Discussion
Region | Model | MSE | MAE | R2 Score
Busan | LSTM | 0.0135 | 0.0556 | 0.9574
 | Bi-LSTM | 0.0146 | 0.0564 | 0.9513
 | Stacked Bi-LSTM | 0.014 | 0.0553 | 0.9560
 | RNN | 0.0225 | 0.1007 | 0.9178
 | GRU | 0.0171 | 0.0656 | 0.9459
Seoul | LSTM | 0.0086 | 0.055 | 0.9256
 | Bi-LSTM | 0.009 | 0.0529 | 0.9386
 | Stacked Bi-LSTM | 0.0076 | 0.0385 | 0.9462
 | RNN | 0.0161 | 0.0759 | 0.8966
 | GRU | 0.0085 | 0.0479 | 0.9361
Gyeonggi | LSTM | 0.0063 | 0.0406 | 0.9527
 | Bi-LSTM | 0.007 | 0.0434 | 0.9488
 | Stacked Bi-LSTM | 0.0062 | 0.0419 | 0.9433
 | RNN | 0.0096 | 0.0672 | 0.8978
 | GRU | 0.0058 | 0.0384 | 0.9503
Gangwon | LSTM | 0.0145 | 0.0599 | 0.9465
 | Bi-LSTM | 0.0178 | 0.0663 | 0.9246
 | Stacked Bi-LSTM | 0.0125 | 0.0491 | 0.9534
 | RNN | 0.0159 | 0.0661 | 0.9389
 | GRU | 0.0143 | 0.0593 | 0.9466
Daejon | LSTM | 0.0127 | 0.0593 | 0.9215
 | Bi-LSTM | 0.0127 | 0.0596 | 0.9333
 | Stacked Bi-LSTM | 0.0118 | 0.0584 | 0.9282
 | RNN | 0.0169 | 0.0756 | 0.8798
 | GRU | 0.0129 | 0.0589 | 0.9293
Gyeongnam | LSTM | 0.0109 | 0.0543 | 0.939
 | Bi-LSTM | 0.0104 | 0.0484 | 0.9459
 | Stacked Bi-LSTM | 0.013 | 0.0593 | 0.9162
 | RNN | 0.0121 | 0.0653 | 0.9269
 | GRU | 0.0111 | 0.0548 | 0.9345
Jeonbuk | LSTM | 0.0161 | 0.0618 | 0.9352
 | Bi-LSTM | 0.0155 | 0.0587 | 0.9394
 | Stacked Bi-LSTM | 0.0153 | 0.0558 | 0.9423
 | RNN | 0.019 | 0.0753 | 0.9217
 | GRU | 0.0161 | 0.0635 | 0.939
Sejong | LSTM | 0.0159 | 0.0642 | 0.9409
 | Bi-LSTM | 0.0155 | 0.0623 | 0.9442
 | Stacked Bi-LSTM | 0.0148 | 0.0573 | 0.9471
 | RNN | 0.0217 | 0.0788 | 0.9167
 | GRU | 0.0157 | 0.0633 | 0.9463
Chungbuk | LSTM | 0.0181 | 0.0714 | 0.885
 | Bi-LSTM | 0.0182 | 0.0678 | 0.8867
 | Stacked Bi-LSTM | 0.0176 | 0.0598 | 0.8982
 | RNN | 0.0242 | 0.0815 | 0.8254
 | GRU | 0.0185 | 0.0695 | 0.8869
Chungnam | LSTM | 0.0099 | 0.0498 | 0.945
 | Bi-LSTM | 0.0095 | 0.0478 | 0.9453
 | Stacked Bi-LSTM | 0.0092 | 0.0441 | 0.9507
 | RNN | 0.0113 | 0.06 | 0.9413
 | GRU | 0.0104 | 0.0576 | 0.9368
The predictions made by five deep learning models and ten regions are displayed in Table 1. The table indicates that the stacked BiLSTM achieves the best performance in all regions. GRU is the second-best model for deep learning, followed by BiLSTM, LSTM, and RNN. Compared to other deep learning models, the stacked BiLSTM has the highest performance because of its architecture, which consists of many layers of BiLSTM.

## Slide 13
Result and Discussion
Prediction Model vs Actual Data

## Slide 14
This work provides a comparison model employing 10 data regions in South Korea with fairly decent findings.
Stacked Bi-LSTM with a single dense layer achieves excellent performance in eight out of ten regions, particularly in the MSE and MAE performance sections.
In the future, we will investigate offering a technique that uses spatial-temporal analysis to produce new predictions using only data from the closest city.
Conclusions

## Slide 15
This work was partly supported by the Technology Development Program of MSS (S3098815) and the MSIT (Ministry of Science and ICT), Korea, under the ITRC(Information Technology Research Center) support program (IITP-2022-2018-0-01396) supervised by the IITP(Institute for Information & Communications Technology Planning & Evaluation).
Acknowledgment

## Slide 16: Thank you